## Slide 1: CDR Infantry Supply Station

## Slide 2: Introduction
Size and limitation of the supply station Supply station size : 1m*1m*1m Specs of bullets: 2.6 g (±5%), plastic, 17 mm (-3% to 0%) in diameter Total number of bullets: 800

## Slide 3
Brief structure of the supply station

## Slide 4
Components for supply station 12V motors: 12V 100RPM high torque DC Motor MCU: Arduino Uno Rev3 Motor Driver: Pololu Simple High-Power Motor Controller 18v15 Detect Sensor: QSD122A4R0-ND & QED123-ND Power source: NIMH Battery 12.0V 2300MAH

## Slide 5: Objective
Be fully automatic
Minimize the filling time
Follow restrictions of the competition
Prevent any jamming of bullets in the station

## Slide 6: Photo Interrupter
Transmission-type photo sensor
  A light emitting elements
  A light receiving elements
  Acting as an optical switch
Infantry Robots Detector
  Signal triggers after infantry robots block infrared light
  Bullets will release from the second stage
Components:
  QED123--- Plastic Infrared Light Emitting Diode
  QSD122--- Plastic Silicon Infrared Phototransistor

## Slide 7: Photo Interrupter Con’t
QED123 : (Emitter)

## Slide 8: Photo Interrupter Con’t
QSD122: (Detector)
The base is left disconnected
Light is used to enable the current flow through the phototransistor.

## Slide 9: Photo Interrupter Con’t
Phototransistor Circuit:
1. Common Emitter phototransistor circuit:
Light is detected
The output moves from a high-voltage state to a low-voltage state.

## Slide 10: Photo Interrupter Con’t
Phototransistor Circuit:
    2. Common Collector phototransistor circuit:
The output that moves from the low- state
to a high-state when light is detected.